## Slide 1: MobilityFirst Project Update FIA PI Meeting, March 18-19 Part-I – Architectural Overview
Arun Venkataramani, Dipankar Raychaudhuri
Umass Amherst, Rutgers

## Slide 2: From Design Goals to Current Architecture
Host + network mobility
No global root of trust
Intentional receipt
Proportional robustness
Content-awareness
Evolvability
Global name service
Name certification
Name resolution
Context & M2M services
Service migration
Content storage & retrieval
Key insight: Logically centralized global name service
enhances mobility, security, and network-layer functions
Inter-,intra-domain
routing
Segmented
transport
Computing
layer
Management
plane

## Slide 3: Architecture: Global name service
Global name service
Name certification
Name resolution: Auspice, DMap
Context & M2M services
Service migration
Content storage & retrieval
human_readable_name  GUID
“Darleen Fisher’s phone”  1A348F76
self-certifying GUID = hash(public-key) permits bilateral authentication
GUID flexibly identifies principals:
interface, device, person, group, service, network, etc.

## Slide 4: Architecture: Global name service
Global name service
Name certification
Name resolution: Auspice, DMap
Context & M2M services
Service migration
Content storage & retrieval
GUID  NA
NA1
NA2
GUIDNA1
resolve(GUID)
data
GUIDNA2
GUIDNA1
GUIDNA2

## Slide 5: Global name service: Content retrieval
Name certification
Name resolution: Auspice, DMap
Context & M2M services
Service migration
Content storage & retrieval
Global name service

## Slide 6: Global name service: Content retrieval
Content CGUID  [NA1, NA2, … ]
  Opportunistic caching + request interception
GNRS
CGUID
[NA1,NA2,…]
CGUID
CGUID
CGUID
CGUID
CGUID
CGUID
NA1
NA2
get(CGUID, NA1)
get(CGUID)

## Slide 7: Global name service: Content retrieval
Name certification
Name resolution: Auspice, DMap
Context & M2M services
Service migration
Content storage & retrieval
Global name service

## Slide 8: Indirection and grouping
Indirection: GUID1  GUID2
Grouping: GUID  {GUID1, GUID2, …, GUIDk}
Indirection and grouping enable context-aware services,
content mobility, and group mobility

## Slide 9: Indirection + grouping: Multicast
MGUID  {T1, T2, …, Tk} (terminal networks)
MGUID  {members(MGUID) | Ti} (late binding)
Global name service
MGUID
{T1,T2,…,Tk}
T1
Tk
T2
send_data(MGUID,T1)
send_data(MGUID,T2)
send_data(MGUID,T3)

## Slide 10: Indirection+grouping: Context-awareness
At source: CAID  {T1, T2, …, Tk} // get terminal networks
At terminal n/w: CAID  {members(CAID) | Ti} // late binding
Global name service
CAID
{T1,T2,…,Tk}
T1
Tk
T2
send_data(CAID,T1)
send_data(CAID,T2)
send_data(CAID,T3)
CAIDmembers(CAID){T1, T2, …, Tk}
GUIDi[Ti,{“type””yellowcab”,“geo””Times Sq.”}]
GUIDiCAID

## Slide 11: Indirection+grouping: Content directories
Moving content directory (CDID) from NA1 to NA2
Global name service
NA1
nbc.com/*
NA2
CDID[NA2]
C1
NA2
get(C1,NA2)
CDIDNA2
  C1{CDID, “name””nbc.com/content1”}

## Slide 12: Group mobility
Group GUIDs help reduce update overhead even when no actual data transfer is happening
Global name service
NA1
NA2
GGUIDNA2
GUID1
NA2
send(GUID1,NA2)
GGUIDNA2
  GUIDiGGUID

## Slide 13: From Design Goals to Current Architecture
Host + network mobility
No global root of trust
Intentional data receipt
Proportional robustness
Content-awareness
Evolvability
Global name service
Name certification
Name resolution
Context & M2M services
Service migration
Content storage & retrieval
Key insight: Logically centralized global name service
enhances mobility, security, and network-layer functions
Inter-,intra-domain
routing
Segmented
transport
Computing
layer
Management
plane

## Slide 14: Architecture: Scaling interdomain routing
NA1
NA2
Function: Route to GUID@NA
Scale: Millions of NA’s  huge forwarding tables
NA3
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
send(GUID@NA, data)
Network | Interface
NA1 | 2
NA2 | 6
NA3 | 1
NA4 | 2
… | …
… | …
NA108 | 4
Notes: 14

## Slide 15: Architecture: Scaling interdomain routing
Function: Route to GUID@NA scalably
Approach: Core and edge networks to reduce state
T1
T2
T3
T4
T5
T6
X2
X3
X1
Global name service
GUID
[X2,T4]
GUID
X2,T4
data
Notes: 15

## Slide 16: Architecture: Multihoming and multipath
Global name service: Multihomed resolution
  GUID_src  {[X3,R1], [X3,R2], … ,[X3,Rm]}
  GUID_dst  {[X1,T1], [X2,T2], [X1,T2], … , [X2,Tk]}
  GUID_dst  {“TE_policy”  “prefer WiFi for delay-tolerant downloads”}
T1
T2
Tk
R1
R2
Rm
X1
X2
X3

## Slide 17: From Design Goals to Current Architecture
Host + network mobility
No global root of trust
Intentional data receipt
Proportional robustness
Content-awareness
Evolvability
Global name service
Name certification
Name resolution
Context & M2M services
Service migration
Content storage & retrieval
Key insight: Logically centralized global name service
enhances mobility, security, and network-layer functions
Inter-,intra-domain
routing
Segmented
transport
Computing
layer
Management
plane

## Slide 18: Architecture: Computing layer
Programmable computing layer enables service flexibility and evolvability
  Routers support new network services off the critical path
  Packets carry (optional) service tags for demuxing
  Integration with “active” GUID resolution in global name service
......
......
Packet forwarding/routing
Computing layer
CPU
Storage
Virtual
Service
Provider
Content
x-coding
Privacy
routing
anon
anon

## Slide 19: From Design Goals to Current Architecture
Host + network mobility
No global root of trust
Intentional data receipt
Proportional robustness
Content-awareness
Evolvability
Global name service
Name certification
Name resolution
Context & M2M services
Service migration
Content storage & retrieval
Key insight: Logically centralized global name service
enhances mobility, security, and network-layer functions
Inter-,intra-domain
routing
Segmented
transport
Computing
layer
Management
plane

## Slide 20: Segmented block transport
Segment = contiguous sequence of links
Storage routers available at segment boundaries
Unit of transmission a named block = large contiguous chunk of data (not small packets as in E2E TCP)
ISP1
ISP3
ISP2
Block
4G
WiFi
Storage
router
Storage
router
Segment 1
Segment 2

## Slide 21: From Design Goals to Current Architecture
Host + network mobility
No global root of trust
Intentional data receipt
Proportional robustness
Content-awareness
Evolvability
Global name service
Name certification
Name resolution
Context & M2M services
Service migration
Content storage & retrieval
Key insight: Logically centralized global name service
enhances mobility, security, and network-layer functions
Inter-,intra-domain
routing
Segmented
transport
Computing
layer
Management
plane

## Slide 22: Management plane
Management plane to enable
  Visibility into network performance metrics
  Access-controlled querying of intradomain state
  Logically centralized decision-making
  Early detection and response to security problems
  Client-assisted collection of management data
AP
Control & Management Plane
Network
Mgmt. API
Data Plane
Data packets

## Slide 23: Architecture: Why logically centralized?
Indirection-based
Logically centralized
Network-layer
Resolution Design traits  | Indirection-based | Logically-centralized | Network-layer
Intial lookup: namelocation | -NA- | Nimrod, LISP, HIP, AIP, HAIR, XIA, MobilityFirst | -NA-
 |  | LNA, DOA, UIP, Codons | 
IP data routing | GSM/MobileIP, i3 | All | DONA, Serval
Named-data routing | i3 | Possible in LNA, DOA, UIP (or DHT schemes) | TRIAD, ROFL, DONA, CCN/NDN, Serval
Mid-session mobility | Seamless | Bilateral, falling back on name service | Seamless; Outage ≈ convergence delays
Worst-case size fwd’ing table for N names | O(#IP prefixes) | O(#IP prefixes), or O(#names/router) per-AS in XIA, MobilityFirst | No aggr: Ω(N) for constant stretch Aggr: O(#displaced IDs)

## Slide 24: Global name service as geo-distributed key-value store
Global name service
resolve(GUID,…)
value(s)
GUID: {
{NAs:[[X1,T1],[X2,T2],…},
{geoloc:[lat, long]},
{TE_prefs: [“prefer WiFi”,…]},
{ACL: {whitelist: […]}},
…
}
resolve(GUID,…)
value(s)

## Slide 25: Auspice design goals
Low response time: Replicas of each name’s resolver should be placed close to querying end-users
Low update cost: Number of resolver replicas should be limited to reduce replica consistency overhead
Load balance: Placement of replicas across all names should prevent load hotspots at any single site
Availability: Sufficient number of replicas so as to ensure availability amidst crash or malicious faults
Consistency: Each name resolver’s consistency requirements must be preserved

## Slide 26: Questions?
http://mobilityfirst.cs.umass.edu
http://mobilityfirst.winlab.rutgers.edu

## Slide 27: Trade-offs of traditional approaches
Replicate everything everywhere:
  + Low response times
  - High update cost under mobility, load imbalance
Few primary replica plus edge caching:
  + Low update bandwidth cost
  - Consistency requirements may limit caching benefits
  - Load balance vs. response time trade-offs
Consistent hashing with replication
  + Good load balance
  - High response times (randomization, locality at odds)
  - Dynamic replication, consistency coordination, load balance

## Slide 28: Auspice replica placement
Locality-aware
Load-aware

## Slide 29: Auspice resolver placement engine
Replica controllers
Active
replicas
X
X
X
X
X
X
X
X
X
X
End-hosts or local name servers
First request for name X
Typical request for name X to nearby active replica
Load reports
Locality-aware,
load-aware,
consistent
Migrate
replicas
Mapping algorithm + Paxos to compute active replica locations

## Slide 30: Auspice service migration (in-progress)
Paxos
Paxos
Paxos
Paxos
Sequential consistency
Lineariazability
create_replica(.)
shutdown_replica(.)
migrate_replica(.)
America
Europe
Asia
report_load(.)
Replica controllers
Service replicas (VMs)

## Slide 31: Auspice implementation & evaluation
Implemented mostly in Java (~22K lines of code)
  Supports mysql, MongoDB, Cassandra, in-memory store
  HTTP API for request/responses
Flexible keys and values
  [GUID, NA], [GUID, IP], [name, IP]
Near-beta version deployed on eight geo-distributed Amazon EC2 locations
  Extensive evaluation on larger clusters and PlanetLab settings
Mobile socket library for seamless mid-session client and server migration

## Slide 32: Auspice vs. alternate proposals

## Slide 33: Auspice vs. commercial managed DNS

## Slide 34: Architecture: Why logically centralized?
Indirection-based
Logically centralized
Network-layer

## Slide 35: Application scenario: Emergency geo-cast
Demo by Emmanuel Cecchet
  http://www.youtube.com/watch?v=tTmOArfXSsw